FINAL REPORT ON THE MRL TURBINE SIMULATION
COURSE OF MODELING TECHNIQUES FOR FLUID MACHINES
A.Y. 2017/2018

immagine
turbina

Marco Belloli
Marco Bonasegale
Alberto Casali
Andrea Rossi
Summary:

        First section

1. Brief description of the the hydraulic turbine and relative input data
2. Cfd workflow applied for the Momentum Reversal and Lift Tidal Turbine that the group has followed along the in-class course of Modeling Techniques for Fluid Machines
  ( Mesh generation steps, turbolence modeling, discretization schemes and results)

        Sensitivity analysis section

1. Mesh Sensitivity analysis with relative power and turbolent viscosity asintotic trend
2. Numeric schemes influence on the domain once optimized mesh is fixed
3. Power coefficient as a function of the BSR
4. Conclusions

MRL Tidal Turbine Description

The MRL Turbine is a hydraulic machine which is able to exploit the upcoming water flow that is passing through the cross sectional area of the inlet of the machine. Momentum Reversal and Lift Tidal Turbine is a cross-
flow tidal-stream device which converts
 the energy of the water
flow into mechanical power.So the most advantageous locations in order to place this device are whatever kind of regular river with a smooth river bed or any sea/ocean areas which are subjected to relevant tidal phenomena.
The turbine is made up of three rotating blades and each blade is subjected to the combination of two rotating motions. A rotation omega0 along the machine axis and a rotation omega1 around the blade individual axis with counter-rotating omega0 and omega1.

The flow-blade interaction leads to a drag force that is coming out while the blade is placed in the upper part of the circumferential path and a lift force on each blade located in the lower part of the path.
The resulting torque multplied by the rotating speed will give the generated power of the turbine which, in the end, is our final useful effect. The generated power per turbine is not really high (a few Watts ) and this is the reason why the “ farm layout” that Prof. Gavin Tabor showed us at the beginning of the course is used. Many little turbines are placed in a schematic and regular disposition in order to extract a higher power from the tidal stream.
Since from the first raw presentation of the machine we can realise that the mesh will have a relevant importance in the representation and validation of this complex rotating movement. We will deal with a rotating mesh which is progressivly refined closeto the blades, ending with the boundary layers when we are approaching the solid walls of the blades.

Input data:

The turbine is surrounded by an upcoming water flow set at 1 m/s constant along y axis.
CAD files were provided by our professor and all the geometry parameters were known.
The in-class workflow has been divided into four little sub-tasks. The sub-tasks allowed us to start to get more familiar with the project work and understand the main issues met along the path with the help of the professors. The in-class project started with the raw mesh generation (blockMesh, snappyHexMesh), continued with the preparation of the rotating mesh(AMI files, baffles creation, merge and split procedure), movement of the mesh with the provided motion laws (real turbine rotation, gif rendering) and finally the set up, running and post processing of the simulation.

Prossima cosa da scrivere (parte progetto in classe)
descrizione mesh e foto
set up di augusto keps ( valutazioni sul keps attraverso yplus), numeric scheme risultati
conclusioni al termine della fase di progetto in classe

parte di analisi nostra

mesh sensitivity e conclusione sui risultati

numeric schemes

conclusioni