FINAL REPORT ON THE MRL TURBINE SIMULATION
COURSE OF MODELING TECHNIQUES FOR FLUID MACHINES
A.Y. 2017/2018

Marco Belloli
Marco Bonasegale
Alberto Casali
Andrea Rossi
Summary:

        First section

1. Brief description of the the hydraulic turbine and relative input data
2. Cfd workflow applied for the Momentum Reversal and Lift Tidal Turbine that the group has followed along the in-class course of Modeling Techniques for Fluid Machines
  ( Mesh generation steps, turbolence modeling, discretization schemes and results)

        Sensitivity analysis section

1. Mesh Sensitivity analysis with relative power and turbolent viscosity asintotic trend
2. Numeric schemes influence on the domain once optimized mesh is fixed
3. Power coefficient as a function of the BSR
4. Conclusions

MRL Tidal Turbine Description

The MRL Turbine is a hydraulic machine which is able to exploit the upcoming water flow that is passing through the cross sectional area of the inlet of the machine. Momentum Reversal and Lift Tidal Turbine is a cross-
flow tidal-stream device which converts
 the energy of the water
flow into mechanical power.So the most advantageous locations in order to place this device are whatever kind of regular river with a smooth river bed or any sea/ocean areas which are subjected to relevant tidal phenomena.
The turbine is made up of three rotating blades and each blade is subjected to the combination of two rotating motions. A rotation omega0 along the machine axis and a rotation omega1 around the blade individual axis with counter-rotating omega0 and omega1.

The flow-blade interaction leads to a drag force that is coming out while the blade is placed in the upper part of the circumferential path and a lift force on each blade located in the lower part of the path.
The resulting torque multplied by the rotating speed will give the generated power of the turbine which, in the end, is our final useful effect. The generated power per turbine is not really high (a few Watts ) and this is the reason why the “ farm layout” that Prof. Gavin Tabor showed us at the beginning of the course is used. Many little turbines are placed in a schematic and regular disposition in order to extract a higher power from the tidal stream.
Since from the first raw presentation of the machine we can realise that the mesh will have a relevant importance in the representation and validation of this complex rotating movement. We will deal with a rotating mesh which is progressivly refined closeto the blades, ending with the boundary layers when we are approaching the solid walls of the blades.

Input data:

The turbine is surrounded by an upcoming water flow set at 1 m/s constant along y axis.
Rotational speed 100 rpm.
CAD files were provided by our professor and all the geometry parameters were known.
The in-class workflow has been divided into four little sub-tasks. The sub-tasks allowed us to start to get more familiar with the project work and understand the main issues met along the path with the help of the professors. The in-class project started with the raw mesh generation (blockMesh, snappyHexMesh), continued with the preparation of the rotating mesh(AMI files, baffles creation, merge and split procedure), movement of the mesh with the provided motion laws (real turbine rotation, gif rendering) and finally the set up, running and post processing of the simulation.

Mesh Generation

One of the most challenging section of the in-class project was the generation of the raw turbine domain mesh. We have used many different openFoam comands in order to build a complete and exhaustive mesh that must be suitable for the hydraulic problem characteristics.
Let’s start to present the overall mesh work-flow with all the brief steps evaluation.
- The scaling of the dimensions and geometry parameters coming from the stl files from millimiters to meters in order to perform correst calculations in the openFoam environment
- blockMesh and snappyHexMesh for each of the three blades. At this point castellated, snapped and layered mesh have been realized for each blade and we have to join all together
- Merging procedure in order to have one complete mesh and the copy of the mesh inside our main environment of the project. We have decided to oparate in this way in order to have a better comunication level in terms of interpolation values among mesh sub-domains. In this way the neighboring cells of different sub-domain are well oriented and aligned. The result is an improvement on the mesh quality controls as non-orthogonality index and skewness coefficient because we have parallel disposition of cells and they appear as concentric refined layers
- Mesh extrusion with the thickness of the 2D domain already given as a geometry parameter equal to the blade width)
- Wall layer refinement
- The first mesh is the “ 40x120” mesh where the couple of numbers indicate the number of squared and regular cells that are disposed in the y and x direction respectively. When we’ll deal with the mesh sensitivity analysis we call ‘mesh xx’ the mesh with xx cells in the y direction only, in order to make the comparison section easier and faster to understand

ALCUNE FOTO DELLA MESH INIZIALE (quella 40x120)

Set up of the in-class project

In the final part of the in-class project we performed the set up and run of the first raw simulation.
To do so, we have to manage with the boundary conditions of the problem, the turbolence modeling and the numeric schemes. All thease macro-section of the simulation were assigned “a priori” and the last part of our work is to play with all these parameters and try to understand the influence of each singular changing in the set up on the final result that the turbine must provide.

First setup turbolence modeling: k-epsilon

Boundary conditions

IMMAGINE BOUNDARY DALLA SLIDE

Boundary conditions are referred to the water stream velocity that is investing the machine, the pressure of the water in the stream channel, k, w and nut values.
Our main interest is to focus the first two boundary conditions so velocity and pressure.

Velocity U

uniform internal field set equal to 1 m/s in x direction even if in the class we set motionless stream at the initial time equal to 0 (starting point of the simulation) amd 1 m/s at the inlet of the domain. We take this decision in order to eliminate transient simulation (which is not in our interest) and work only on the regime condition (where we computee forces and output power)

Now if we consider our prismatic domain made of 6 walls we can distinguish into:

- inlet section. The water is entering in the domain through this inlet surface,moving towards x direction from the left to the right side of the domain. The boundary condition we set here is fixed value. This fixed value is equal to 1 as said before
- outlet section. Water is exiting from the domain and at this point the fluid has faced the machine and resulting stream is all but not constant along this section. We can’t set fixed value boundary condition otherwise we force the solution. What we choose is zeroGradient
- front wall. Empty boundary condition so we say to the solver not to solve the fluid dynamic equations along this wall (no fluid flux through the front wall)
- back wall. Same considerations for the front wall
- upper wall. slip
- lower wall. No slip (equivalent to fixed value =0)
- blades. MovingWallVelocity (default boundary condition for the blades)
- ami interfaces. CyclicAMI (default boundary condition for the ami components)

Pressure P

- inlet section. zeroGradient
- outlet section. FixedValue uniform equal to 0 ( no gravitational force is taken into account)
- front wall. Empty
- back wall. Empty
- upper wall. Fixed value uniform =0
- lower wall. zeroGradient
- blades. ZeroGradient
- ami interfaces. CyclicAMI

k (turbolent kinetic energy):

default settings. Wall function used close to the blade and lower walls

epsilon (dissipation rate):

default settings

nut ( turbolent viscosity):

defaul settings. ( in the next section we will use an already computed value of nut found during the evaluation of simulations in order to deal with a regime value of nut because we are interested in the regime fluid dynamic behavior of the turbine). Nut wall function used close to blade and lower wall

Numeric schemes:

default numeric schemes

Solver:

pimpleDynamicFoam in PISO mode with nOuter correctors 1 and nInner correctors 2

\todo{} INSERIRE IMMAGINI DI FORZE COPPIA , POTENZA E RESIDUI DEL CASO STANDARD CIOE QUELLO A FINE CORSO CON 40 CELLE IN Y E TUTTE LE OPZIONI DI BASE GRAFICO DI Y+ CHE NON VA BENE PER IL MODELLO KEPSILON

Rielaboration section

In this second part we’re dealing with the discussion of all the setting parameters that we have chosen in the in-class project. Our objective is to understand what are the most advantageous parameters to use that lead to the most reliable results. We’re investigating the mesh control parameters, the turbolence modeling (linear, k-epsilon, kw-sst), the numeric schemes (first order, second order), the contribution of the gravitational force and the evaluation of the power coefficient as a function of the Blade Speed Ratio (BSR).

Mesh sensitivity analysis

Our sensitivity analysis campare different refinement levels of the mesh from the coarser to the finer one. The analysis is performed for the following meshes:
- mesh 20
- mesh 40
- mesh 60
- mesh 80
- mesh 120
- mesh 160

We have chosen thease mesh levels because they cover the doubling of the number of the cells in the x and y direction for the 2D domain analysis. The coarser mesh 20 is made of a number of cells close to 10 thousand so the first level of doubling of the cells is around 40 thousand (x2 in x direction and x2 in y direction). Mesh 60 has this number of cells while the second doubling level occurs at about 160 thousand cells and mesh 160 is roughly composed by such amount of cells.

Despite the power indication is not the best parameter to highlight the sensitivity behavior, it is the desired output parameter of our simulation and the one that we are more interested in so it will be put beside the total pressure drop computed at inlet and outlet section of the domain at the end of the simulation (at 2.4 s).